## Slide 1
Speaker : Ricardo Gallo (Believe Green LLC, Chicago, USA)
GENERAL FUSION - Vancouver, Canada
Magnetized Target Fusion (MTF)
NFR-13

## Slide 2
INDEX
October 26
Introduction
How General Fusion’s Magnetized Target Fusion (MTF) approach works
The four stages of the MTF process
Why magnetize the plasma before compressing it
How does mechanical compression heat the plasma
What is the role of liquid metal
Is General Fusion's MTF machine already using this complete system?
5.1 Commercial MTF concept
5.2 LM26 demonstration machine
How does MTF compare with a tokamak and inertial confinement?
The main engineering challenge
In summary

## Slide 3
Introduction
How General Fusion’s Magnetized Target Fusion (MTF) approach works
General Fusion’s approach combines two different ideas in nuclear fusion: magnetic confinement of a plasma and rapid mechanical compression of that plasma to reach fusion conditions.
The Canadian company General Fusion calls this approach Magnetized Target Fusion (MTF). Its central idea is to create a magnetically confined plasma, then compress it using a mechanically driven liquid-metal system, rather than relying exclusively on powerful magnetic fields to confine the plasma for a long time or on lasers to implode a fuel capsule.
In simple terms:
Magnetize the fuel → compress it mechanically → heat it to fusion conditions → extract the energy.
This is an intermediate approach between conventional magnetic-confinement fusion, such as a tokamak, and inertial-confinement fusion, such as laser-driven fusion at the National Ignition Facility.